## Slide 1: Hardware Software Platforms Project Presentation
Servomotor Control with DE1-SoC
Elora Amorison & Clelia Galvanin elora.amorison@student.umons.ac.be
Clelia.galvanin@student.umons.ac.be

## Slide 2: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 3: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 4: Context and Objectives
This project is part of the course Hardware/Software Platforms for students in first master in Electrical Engineering at the Faculty of Engineering of Mons
Objectives:
  To handle an entire electronical project
  To familiar us with processors De-SoC
  To control a Servomotor
  To understand the VHDL coding language
  To create a tutorial for other users

## Slide 5: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 6: Software to install
Quartus II
  http://fpgasoftware.intel.com/?edition=lite
  To install the software, you’ll need both the Quartus software tarfile, and the CycloneV qdz file.
  Save these both to the same directory.
ModelSim
  Select also the “ModelSim-Altera Starter Edition”.
  ModelSim is a HDL Simulator and will be used to simulate signals before using the board.

## Slide 7: Hardware to install
DE1-SoC
  https://www.terasic.com.tw/cgi-bin/page/archive.pl?Language=English&No=836
  In the package, you can find the cable to supply the FPGA and an other one to connect to the computer

## Slide 8: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 9: Create a new project on Quartus
Open Quartus II
Click on “Create a new project”
A new window will open
  Select the folder and the title of your project
  Next
  Click on “empty project”

## Slide 10: Create a new project on Quartus
A window “Family & Device Settings” will open
  Select the right family of your component and then “next”
Here, it is a Cyclone V
5CSEMA5F31C6N

## Slide 11: Create a new project on Quartus
Create new file
  Create a new file at your project and select the VHDL Type File
  You can also add an existing file at your project

## Slide 12: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 13: Servomotor
What is a servomotor ?
  Electrical device, that rotate a part of its body
  with high efficiency and great precision to a
  particular angle between 0 and 180°)
How to connect a servomotor?
  Three cables
  The yellow wire connected to the pin of the board: GPIO1(1)
  The red wire connected to 5V on the board GPIO1(10)
  The brown (or black) wire connected to the ground on the board GPIO1(11)

## Slide 14: Servomotor

## Slide 15: Bloc Diagram to Control a Servomotor
  The values of the position came from the Switch of the board
  The control signal goes to the GPIO1(1) pin and then directly to the servomotor

## Slide 16: Connection between the board and the motor

## Slide 17: Servomotor
How it works?
  Coding a square wave of different pulse width
  Period of 20 ms
  Minimal value of 0,5ms and maximal value 2,5ms

## Slide 18: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 19: Board Control
How to link the hardware and the software?
  Connect the board to the computer
  Create a file to connect the signals with the pins of the board
  To have a look
  at all the pins
  of your board
  you can click on
  this icone

## Slide 20: Board Control
How to put the code on the processor?
  Click on the Program Device

## Slide 21: Board Control
How to put the code on the processor?
  A window will open
  Click on “Hardware Setup” and choose your harware

## Slide 22: Board Control
How to put the code on the processor?
  Click on “Auto Detect” and choose your correct device
  Then on “Add File” and select your own file
  Finally, click on “Start” and wait for the loading of your code

## Slide 23: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 24: Simulations
Driver Simulation
For the simulation, we define some values for the variable « pos ».
We can see the control signal becoming bigger and bigger.
We can zoom to see the value of PWM and so, the PWM value for an 80° angle is 1749440 ns.

## Slide 25: Simulations
Driver+Application Simulation
We change the values of switchs and therefore pos after 3 PWM half period = 3*10ms
We wait for 3 additional PWM half period before pressing the button.
We wait for 1 additional PWM half period before releasing the button.
When the button is released -> switchs values go to Ipos_after.
PWM value is then modified from the next impulse.
We notice that the PWM value increases according to the angle.

## Slide 26: Simulations
Driver+Application Simulation
We make a zoom to measure PWM values and check that the values are growing
proportionnaly with the angle.
Wa can see that the PWM value for an 40° angle is 1 124 640ns and for an 80° angle
is 1 749 440ns (which is equal to our previous value.)

## Slide 27: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 28: Results
Results on an oscillator
Results on the servomotor
  See the video

## Slide 29: Contents
Context and Objectives
Software and Hardware installation
  Software to install
  Board installation
Tests with the board and LabView
  Creating a new project
  Servo-motor
  Board Control
  Simulations
  Results
Software operation

## Slide 30: Software Operation
Diagram block of the behaviour of our program

## Slide 31: Conclusion
Congrats !
You can now drive a servo-motor with a new processor!

## Slide 32: Useful links
Github:
https://github.com/cleliagal/Control-of-Servo-motor-with-DE1-SoC
Youtube Video:
https://www.youtube.com/watch?v=HVyE35rkSaQ